|  | OLDSMOBILE GENERAL SPECIFICATIONS | ¦engine¦ |
| --- | --- | --- |

Engine

| Year | Engine | Carb | Bore and Stroke | Piston Dis place ment Cubic Inches | Com pres sion Ratio (Stan dard) | Maximum Brake H.P. @ R.P.M. | Maximum Torque Lbs. Ft. @ R.P.M. | Normal Oil Press Lbs | Spark Plug Type | Spark Plug Gap | Point Gap adj in to misfire then out | Dwell Angle | Firing Order | Ignition Timing BTDC or Mark | Grnd +/- Volts |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1962 | 155 H.P. F85 | V8-215 | 1 Barrel | 3.5 x 2.8 | 215 | 8.75 | 155 @ 4800 | 210 @ 3200 | 30 | AC 46FFX | .040 | .019 | 30 | 18436572 | 5°/7° auto | -12 |
|  | 185 H.P. F85 | V8-215 | 4 Barrel | 3.5 x 2.8 | 215 | 10.25 | 185 @ 4800 | 230 @ 3200 | 30 | AC 45FF | .040 | .019 | 30 | 18436572 | 5°/7° auto | -12 |
|  | 215 H.P. F85 | V8-215 | 1 Barrel | 3.5 x 2.8 | 215 | 10.25 | 215 @ 4600 | 300 @ 3200 | 30 | AC 45FF | .025 | .019 | 30 | 18436572 | 10° | -12 |
|  | 260 H.P. | V8-394 | 2 Barrel | 4.125 x 3.688 | 394 | 8.75 | 260 @ 4400 | 410 @ 2400 | 35-45 | AC 45 | .030 | .019 | 30 | 18736542 | 2 1/2° | -12 |
|  | 280 H.P. | V8-394 | 4 Barrel | 4.125 x 3.688 | 394 | 10.25 | 280 @ 4400 | 430 @ 2400 | 35-45 | AC 44 | .030 | .019 | 30 | 18736542 | 5° | -12 |
|  | 330 H.P. | V8-394 | 4 Barrel | 4.125 x 3.688 | 394 | 10.25 | 330 @ 4600 | 440 @ 2800 | 35-45 | AC 44 | .030 | .019 | 30 | 18736542 | 5° | -12 |
|  | 345 H.P. | V8-394 | 4 Barrel | 4.125 x 3.688 | 394 | 10.5 | 345 @ 3800 | 440 @ 3200 | 35-45 | AC 44 | .030 | .019 | 30 | 18736542 | 5° | -12 |